## Slide 1
HiPEAC 2024
Accelerating Profile Hidden Markov Models for Fast and Energy-Efficient Genome Analysis
ApHMM
Paper
Kamlesh Pillai, Gurpreet S. Kalsi, Bharathwaj Suresh, Damla Senol Cali, Jeremie S. Kim, Taha Shahroodi, Meryem Banu Cavlak, Joël Lindegger, Mohammed Alser, Juan Gómez Luna, Sreenivas Subramoney, Onur Mutlu
Can Firtina
canfirtina@gmail.com
https://cfirtina.com

## Slide 2: Executive Summary
Key Results: Our ASIC implementation compared to CPU, GPU, and FPGA baselines across 3 workloads
  15.55×–260.03×, 1.83×–5.34×, and 27.97× better performance
  Up to 2622.94× reduction in energy consumption
ApHMM: the first flexible and hardware-software accelerator for pHMMs that can
Substantially reduce unnecessary data storage, data movement, and computations by effectively co-designing hardware and software together
Provide a flexible design to support several genomics workloads that use pHMMs
Goal: Enable rapid, power-efficient, and flexible use of pHMMs for genomics workloads
Problem: The parameters used in pHMMs are mainly trained and used with a computationally intensive Baum-Welch algorithm, causing major performance and energy overhead for many genomics workloads
Motivation: Graph structures such as profile Hidden Markov Models (pHMMs) are commonly used to accurately analyze biological sequences
https://github.com/CMU-SAFARI/ApHMM-GPU

## Slide 3: Outline
Conclusion
Background & Problem
Motivation and Goal
Experimental Methodology
Temperature Analysis
Aggressor Row Active Time Analysis
Spatial Variation Analysis
Implications on Attacks and Defenses
Conclusions
Evaluation
ApHMM

## Slide 4: Genome Analysis – Why?
Fast and accurate genome analysis is important for:
Understanding genetic variations, species, and evolution
Surveillance of disease outbreaks
Predicting the presence of pathogens in an environment
Personalized medicine

## Slide 5: Background: Genome Analysis – How?
Genome sequencing machines can quickly convert biological molecules
  Into sequences of characters for analysis
AAGCTTCCATGG
AAATGGGCTTTC
GCCCAAATGGTT
GCTTCCAGAATG
Sequences from DNA
Biological Molecule (e.g., DNA)

## Slide 6: Sequence Comparison is Essential
Analyze sequences by accurately and quickly comparing them
  To each other
  To a template sequence representative of a species, a certain group…
Essential to understand functionality of a sequence, mutations, diseases…
Biological Sequences
(e.g., DNA, proteins)

## Slide 7: Graphs for Sequence Comparisons
Graphs are commonly used in sequence comparisons
  Can avoid redundant comparisons and storage
  Provides rich information on expected variations between sequences
Biological Sequences
(e.g., DNA, proteins)

## Slide 8: Profile Hidden Markov Models
Profile Hidden Markov Models (pHMMs) are powerful and common graph structures for sequence comparison
  Goal: Identify variations between sequences probabilistically
  Each state outputs a biological character (emission) when visited
  States are visited via transitions (edges) based on observed variations
  Variations: No variation
A
C
T
T
Observed Sequence #1: ACTT
(No variation)
Expected sequence: ACTT

## Slide 9: Profile Hidden Markov Models
Profile Hidden Markov Models (pHMMs) are powerful and common graph structures for sequence comparison
  Goal: Identify variations between sequences probabilistically
  Each state outputs a biological character (emission) when visited
  States are visited via transitions (edges) based on observed variations
  Variations: No variation, Substitutions
Observed Sequence #2: ACTG
(Substitutions)
A
C
T
G
Expected sequence: ACTT

## Slide 10: Profile Hidden Markov Models
Profile Hidden Markov Models (pHMMs) are powerful and common graph structures for sequence comparison
  Goal: Identify variations between sequences probabilistically
  Each state outputs a biological character (emission) when visited
  States are visited via transitions (edges) based on observed variations
  Variations: No variation, Substitutions, Insertions
Observed Sequence #3: AGGGCTT
(I: Insertions)
A
C
T
T
I
Expected sequence: ACTT

## Slide 11: Profile Hidden Markov Models
Profile Hidden Markov Models (pHMMs) are powerful and common graph structures for sequence comparison
  Goal: Identify variations between sequences probabilistically
  Each state outputs a biological character (emission) when visited
  States are visited via transitions (edges) based on observed variations
  Variations: No variation, Substitutions, Insertions, Deletions
Observed Sequence #4: ATT
(D: Deletions)
A
C
T
T
D
Expected sequence: ACTT

## Slide 12: Profile Hidden Markov Models
Profile Hidden Markov Models (pHMMs) are powerful and common graph structures for sequence comparison
  Goal: Identify variations between sequences probabilistically
  Each state outputs a biological character (emission) when visited
  States are visited via transitions (edges) based on observed variations
  Variations: No variation, Substitutions, Insertions, Deletions
Observed Sequence #1: ACTT
Observed Sequence #2: ACTG
Observed Sequence #3: AGGGCTT
Observed Sequence #4: ATT
…
A
C
T
T
D
I
I
I
I
D
D

## Slide 13: Probabilities in pHMMs
Profile Hidden Markov Models (pHMMs) are powerful and common graph structures for sequence comparison
  Goal: Identify variations between sequences probabilistically
A
C
T
T
D
I
I
I
I
D
D
A: 0.1
T: 0.2
G: 0.6
C: 0.1
A: 0.9
T: 0.1
G: 0.0
C: 0.0
A: 0.1
T: 0.1
G: 0.1
C: 0.7
A: 0.2
T: 0.2
G: 0.2
C: 0.4
0.2
0.4
0.7
0.6
0.3
0.1

## Slide 14: Utilizing Probabilities in pHMMs
The Baum-Welch algorithm is commonly used with pHMMs
  For both inference and training by effectively utilizing the probabilities
Inference: Identifying the variations between sequences
Training: Maximizing parameters to observe certain variations
Forward Calculations
Backward Calculations
Updating Transition Probabilities
Updating Emission Probabilities

## Slide 15: Utilizing Probabilities in pHMMs
The Baum-Welch algorithm is commonly used with pHMMs
  For both inference and training by effectively utilizing the probabilities
Inference: Identifying the variations between sequences
Training: Maximizing parameters to observe certain variations
Forward Calculations
Backward Calculations
Updating Transition Probabilities
Updating Emission Probabilities

## Slide 16: Utilizing Probabilities in pHMMs
The Baum-Welch algorithm is commonly used with pHMMs
  For both inference and training by effectively utilizing the probabilities
Inference: Identifying the variations between sequences
Training: Maximizing parameters to observe certain variations
Forward Calculations
Backward Calculations
Updating Transition Probabilities
Updating Emission Probabilities
Training Step

## Slide 17: Forward & Backward Calculations
A dynamic programming approach
  Calculate the ‘possibility’ of visiting each state in a pHMM
  Given an observed sequence (from both directions of the sequence)
A
T
G
T
Forward Calculations
Observed Sequence: ATGT
Backward Calculations
A
D
I
D
C
I
D
T
I
A
D
I
D
C
I
D
T
I
A
T
G
T

## Slide 18: Inference using pHMMs
Goal: Identifying the variations between sequences
  Inference by using decoding algorithms (e.g., the Viterbi Algorithm)
A
T
G
T
Forward Calculations
Observed Sequence: ATGT
Backward Calculations
A
D
I
D
C
I
D
T
I
A
D
I
D
C
I
D
T
I
A
T
G
T
A
C
T
T
D
G
Inference:

## Slide 19: Training using pHMMs
Goal: Maximizing parameters to observe certain variations
  Training using the parameter updating steps in the Baum-Welch algorithm
A
T
G
T
Forward Calculations
Observed Sequence: ATGT
Backward Calculations
A
D
I
D
C
I
D
T
I
A
D
I
D
C
I
D
T
I
A
T
G
T
Training

## Slide 20: pHMMs in Genomics Workloads
pHMMs are commonly used in many genomics applications
1. Error Correction
GCCCATATGGTTAAGCTT
CCCT
TGCT
GCTA
CCTA
GCTT
ATGC
AAGC
CCCT
GCTT
GCCCTTATGCTTAAGCTA
2. Protein Family Search
Protein
Protein
Family #1
Protein
Family #2
3. Multiple Sequence Alignment
GCCC-TATGGTTAAGCTT
GCCCATATGATTAAGCTT
GCCCATATGGTTAAGCTT
GCCCATATGGTTAAGCTT
GCCCGTATGGTT---GCTT
GCCCATATGCTTAAGCTT
GCCC---TGGTTAAGCT--T
GCCCATATCCTTAAGCTT

## Slide 21: The Baum-Welch Algorithm is Costly
The Baum-Welch algorithm causes a major computational overhead in genomics workloads
  Taking up from 46% to 99% of the overall execution time
  Computationally complex dynamic programming calculations
  Compute intensive many floating-point operations
45.76%
51.44%
98.57%

## Slide 22: Existing Solutions are Ineffective
pHMMs are specialized version of Hidden Markov Models (HMMs) with fixed patterns on states and transitions
Generic HMM accelerators cannot exploit the fixed data dependency pattern of pHMMs
A
T
G
T
Forward Calculations in pHMMs
A
D
I
D
C
I
D
T
I
Forward Calculations in HMMs
A
D
I
D
C
I
D
T
I
A
T
G
T

## Slide 23: Existing Solutions are Inflexible
pHMM requirements can change based on the application
  Different pHMM designs:
  Different alphabet sizes: DNA (4 letters), protein (20 letters)
A
C
T
T
D
I
I
I
I
D
D
A
C
T
T
I
I
I
I
Lack of flexible mechanisms to handle different design choices

## Slide 24: Existing Solutions are Inefficient
Suboptimal vectorization of SIMD-based solutions on CPUs and GPUs
  High warp divergence, branching, low port utilization…
A significant portion of the floating-point operations in dynamic programming is redundant
  Same multiplications results can redundantly be computed during training
  Unnecessary data movements
Existing solutions provide suboptimal solutions due to inefficient hardware or software design

## Slide 25: The Problem
SIMD-based solutions on CPUs and GPUs provide suboptimal vectorization
  High warp divergence, branching, low port utilization…
A significant portion of the floating-point operations in DP is redundant
  Same multiplications appear repeatedly due to constant values during training
  Unnecessary data movements
Hardware- or software-only solutions are not sufficient for effectively accelerating pHMMs
The Baum-Welch algorithm causes major performance overhead in important genomics applications

## Slide 26: Outline
Conclusion
Background & Problem
Motivation and Goal
Experimental Methodology
Temperature Analysis
Aggressor Row Active Time Analysis
Spatial Variation Analysis
Implications on Attacks and Defenses
Conclusions
Evaluation
ApHMM

## Slide 27: Goal
Enable rapid, power-efficient, and flexible use of pHMMs when using the Baum-Welch algorithm

## Slide 28
ApHMM
The first flexible hardware-software co-designed acceleration framework that can significantly reduce the computational overhead of the Baum-Welch algorithm for pHMMs
ApHMM-GPU: The first GPU implementation of the Baum-Welch algorithm for pHMMs

## Slide 29: Key Software & Hardware Optimizations
SW
HW
Minimize redundant data storage by efficient pipelining
Reduce unnecessary computations with quick filtering
Avoid repeated operations by utilizing lookup tables
Reduce data movement by exploiting fixed data pattern
Flexible and efficient control logic and hardware design

## Slide 30: Key Software & Hardware Optimizations
SW
Minimize redundant data storage by efficient pipelining
Reduce unnecessary computations with quick filtering
Avoid repeated operations by utilizing lookup tables

## Slide 31: SW: Minimizing Redundant Storage
Observation: Filling the entire Backward table is unnecessary
  Pipelining opportunities to directly consume a Backward value
A
T
G
T
Forward Calculations
Observed Sequence: ATGT
Backward Calculations
A
D
I
D
C
I
D
T
I
A
D
I
D
C
I
D
T
I
A
T
G
T
Training

## Slide 32: SW: Minimizing Redundant Storage
Observation: Filling the entire Backward table is unnecessary
  Pipelining opportunities to directly consume a Backward value
A
T
G
T
Forward Calculations
Observed Sequence: ATGT
Backward Calculations
A
D
I
D
C
I
D
T
I
A
D
I
D
C
I
D
T
I
A
T
G
T
Training
✓
Needed
No need

## Slide 33: SW: Minimizing Redundant Storage
Observation: Filling the entire Backward table is unnecessary
  Pipelining opportunities to directly consume a Backward value
  Partial compute approach: Only a single row should be fully stored
A
T
G
T
Forward Calculations
Observed Sequence: ATGT
Backward Calculations
A
D
I
D
C
I
D
T
I
A
D
I
D
C
I
D
T
I
A
T
G
T
Training

## Slide 34: SW: Minimizing Redundant Storage
Observation: Filling the entire Backward table is unnecessary
  Pipelining opportunities to directly consume a Backward value
  Partial compute approach: Only a single row should be fully stored
A
T
G
T
Forward Calculations
Observed Sequence: ATGT
Backward Calculations
A
D
I
D
C
I
D
T
I
A
D
I
D
C
I
D
T
I
A
T
G
T
Training

## Slide 35: SW: Minimizing Redundant Storage
Observation: Filling the entire Backward table is unnecessary
  Pipelining opportunities to directly consume a Backward value
  Partial compute approach: Only a single row should be fully stored
  Reduces the storage requirements during training
A
T
G
T
Forward Calculations
Observed Sequence: ATGT
Backward Calculations
A
D
I
D
C
I
D
T
I
A
D
I
D
C
I
D
T
I
A
T
G
T
Training

## Slide 36: SW: Reducing Unnecessary Computations
Observation: ‘Negligible’ cells can be ignored without significantly reducing overall accuracy
  Filtering: Non-negligible states are identified by sorting
  Sorting to find exactly states with largest Forward or Backward values
Sorting is complex to implement in hardware (and costly)
  Can we filter without sorting?
A
T
G
T
Forward Calculations
A
D
I
D
C
I
D
T
I
Filtered Forward Calculations
A
D
I
D
C
I
D
T
I
A
T
G
T
Filter by sorting

## Slide 37: SW: Reducing Unnecessary Computations
Observation: ‘Negligible’ cells can be ignored without significantly reducing overall accuracy
  Goal: Find at least states with largest Forward and Backward values
  Histogram-based filtering: Placing the states into buckets corresponding to a range of values
  Filter is full as soon we find at least states (e.g., )
Filter is full
Histogram Filter
.
.
.
8, 9
10, 14
15, 16, 18
11, 20, 21, …
13, 17, 19, …
States
Range
1.00 – 0.94
0.94 – 0.88
0.88 – 0.82
0.82 – 0.76
0.76 – 0.70
0.06 – 0.00
.
.
.
The rest is ignored from further calculation
Filter size = 2 < 10
Filter size = 4 < 10
Filter size = 7 < 10
Filter size = 13 > 10

## Slide 38: SW: Avoiding Repeated Operations
Observation: Same multiplications are redundantly performed
  Same default values are used for each possible connection in pHMMs
  Fixed connection patterns generate a fixed set of multiplication results
Goal: Avoid redundant computations
  By enabling efficient reuse of the common multiplications results
A: 0.1
T: 0.2
G: 0.3
C: 0.4
0.6
A
A: 0.1
T: 0.2
G: 0.3
C: 0.4
0.6
T
A: 0.1
T: 0.2
G: 0.3
C: 0.4
0.6
T
…
…
Costly FP Operations
Same output

## Slide 39: SW: Avoiding Repeated Operations
Observation: Same multiplications are redundantly performed
  Same default values are used for each possible connection in pHMMs
  Fixed connection patterns generate a fixed set of multiplication results
Goal: Avoid redundant computations
  By enabling efficient reuse of the common multiplications results
  Lookup tables (LUTs) to efficiently store and use these common results
A: 0.1
T: 0.2
G: 0.3
C: 0.4
0.6
A
A: 0.1
T: 0.2
G: 0.3
C: 0.4
0.6
T
A: 0.1
T: 0.2
G: 0.3
C: 0.4
0.6
T
…
…
Cheap LUTs
Same output

## Slide 40: Key Software & Hardware Optimizations
SW
HW
Minimize redundant data storage by efficient pipelining
Reduce unnecessary computations with quick filtering
Avoid repeated operations by utilizing lookup tables
Reduce data movement by exploiting fixed data pattern
Flexible and efficient control logic and hardware design

## Slide 41: Overview of ApHMM Design
ApHMM Core
Compute Block
Control Block
LUT
Transition Scratchpad
Histogram
Filter
Data Control
Parameters
Index Control
Calculate Backward (Step-by-Step)
Memory (DRAM/L2/L1)
CPU
Calculate Forward (Full)
Flexible and efficient control logic and hardware design
enables opting out from heuristics and supporting different pHMM designs
✓
Update Emission Probabilities
(Step-by-Step)
Update Transition Probabilities
(Step-by-Step)

## Slide 42: Computing the Baum-Welch in ApHMM
Compute Block
Update Emission (UE)
Calculate Emission
Numerator
Calculate Emission
Denominator
Division & Update Emission
Calculate Forward/Backward & Update Transition
Write Selector
PE Group
#1
Register
PE Group
#1
Register
PE Group
#1
Register
PE Group
#1
Register
PE Group
#1
Register
PE Group
#1
Register
PE Group
#1
Register
PE Group
#1
Register
PE Group #1
PE Engine #1
PE Engine #1
PE Engine #1
PE #1
PE #1
Index Control
Efficiently exploiting data locality, broadcasting, memoization, streaming, and pipelining with our SW optimizations for an effective HW-SW co-design
✓
Forward/
Backward (PE)
Previous Step Coefficients (L1):
or (Broadcasting)
or
LUT
Update Transition (UT)
Previous Transition Numerator
8KB Transition Scratchpad
MUL
ADD
FP DIV
Dot Product Tree
Accumulator
Reduction Tree
or
,
TE MUL

## Slide 43: Outline
Conclusion
Background & Problem
Motivation and Goal
Experimental Methodology
Temperature Analysis
Aggressor Row Active Time Analysis
Spatial Variation Analysis
Implications on Attacks and Defenses
Conclusions
Evaluation
ApHMM

## Slide 44: Evaluation Methodology
Performance, Area, and Power Analysis:
  Synthesized SystemVerilog Model in a 28nm process @1GHz
  CPU baseline: AMD EPYC 7742 @2.26GHz (1, 12, 32 threads)
  GPU baselines: Titan V & A100
  FPGA baseline: FPGA D&C
Use cases and their software baseline:
  Error Correction – Apollo
  Protein Family Search – HMMER
  Multiple Sequence Alignment – HMMER

## Slide 45: Evaluation Methodology
Comparison Points
  CPU: Apollo, HMMER
  GPU: ApHMM-GPU, HMM_cuda
  FPGA: FPGA D&C
Datasets
  Error correction: Real 10,000 DNA sequences from Escherichia coli (E. coli) with average 5,128 read length
  Protein family search: Entire Pfam database (19,632 pHMMs) and real 214,393 protein sequences from Mitochondrial carrier
  Multiple sequence alignment: Aligning over ~1 million protein sequences from Pfam database

## Slide 46: Performance: The Baum-Welch Algorithm
15.55×–260.03×, 1.83×–5.34×, and 27.97× faster than the CPU, GPU, and FPGA implementations of the Baum-Welch algorithm
GPUs provide better performance for Forward calculations due to frequent off-chip memory accesses in ApHMM during Forward calculation

## Slide 47: Performance: Workload Acceleration
1.29×–59.94×, 1.03×–1.75×, and 1.03×–1.95× better performance compared to the CPU, GPU, and FPGA baselines
Error correction benefits most from the acceleration due to frequent and costly training

## Slide 48: Energy: Overall Comparisons
For the Baum-Welch algorithm: 2474.09× and 896.70×–2622.94× reduction in energy consumption compared to CPU-1 and GPU implementations
For the workloads: 64.24×, 1.75×, and 1.96× reduction compared to CPU-1

## Slide 49: Speedup of Each Optimization
We analyze the speedup that each optimization provides over the CPU baseline
Broadcasting and partial compute together is only possible with an efficient HW-SW co-design

## Slide 50: Area and Power
We analyze the area and power for ApHMM-4 using the Synopsys Design Compiler with a 28nm process @1GHz:
UTs require the largest area due to several complex units such as multiplexer, division pipeline, and local memory
ApHMM can significantly accelerate pHMMs with relatively small area and power requirements

## Slide 51: More in the Paper
More Results
  Detailed discussion on the results generated per use case
  Justification of the dataset and baseline choices
Details of all mechanisms and configurations
  Details of our design space exploration
  Data distribution and memory layout
  Control and execution flow of ApHMM cores
  Related work discussion (e.g., Pair HMMs vs pHMMs)
  Detailed background on the equations and algorithms

## Slide 52: ApHMM
Can Firtina, Kamlesh Pillai, Gurpreet S. Kalsi, Bharathwaj Suresh, Damla Senol Cali, Jeremie S. Kim, Taha Shahroodi, Meryem Banu Cavlak, Joël Lindegger, Mohammed Alser, Juan Gómez Luna, Sreenivas Subramoney, and Onur Mutlu, "ApHMM: Accelerating Profile Hidden Markov Models for Fast and Energy-Efficient Genome Analysis” ACM TACO, Dec 2023. [Online link at ACM TACO] [arXiv preprint] [ApHMM Source Code]

## Slide 53: ApHMM-GPU Source Code
https://github.com/CMU-SAFARI/ApHMM-GPU

## Slide 54: Outline
Conclusion
Background & Problem
Motivation and Goal
Experimental Methodology
Temperature Analysis
Aggressor Row Active Time Analysis
Spatial Variation Analysis
Implications on Attacks and Defenses
Conclusions
Evaluation
ApHMM

## Slide 55: Conclusion
Key Results: Our ASIC implementation compared to CPU, GPU, and FPGA baselines across 3 workloads
  15.55×–260.03×, 1.83×–5.34×, and 27.97× better performance
  Up to 2622.94× reduction in energy consumption
ApHMM: the first flexible and hardware-software accelerator for pHMMs that can
Substantially reduce unnecessary data storage, data movement, and computations by effectively co-designing hardware and software together
Provide a flexible design to support several genomics workloads that use pHMMs
Goal: Enable rapid, power-efficient, and flexible use of pHMMs for genomics workloads
https://github.com/CMU-SAFARI/ApHMM-GPU

## Slide 56
HiPEAC 2024
Accelerating Profile Hidden Markov Models for Fast and Energy-Efficient Genome Analysis
ApHMM
Paper
Kamlesh Pillai, Gurpreet S. Kalsi, Bharathwaj Suresh, Damla Senol Cali, Jeremie S. Kim, Taha Shahroodi, Meryem Banu Cavlak, Joël Lindegger, Mohammed Alser, Juan Gómez Luna, Sreenivas Subramoney, Onur Mutlu
Can Firtina
canfirtina@gmail.com
https://cfirtina.com

## Slide 57
Backup Slides
Motivation and Goal
Experimental Methodology
Temperature Analysis
Aggressor Row Active Time Analysis
Spatial Variation Analysis
Implications on Attacks and Defenses
Conclusions

## Slide 58: Why Graphs are Useful
Accurate comparison requires identifying changes (insertions, deletions, substitutions) between sequences due to
  Variations between individuals and template sequences
  Errors in sequences
How to avoid unnecessary (and costly) comparisons?
Variants?
Which variant?
Erroneous analysis?
Errors?

## Slide 59: Filtering – Performance Benefits
Filtering heuristics aim to reduce unnecessary computations
Motivational Study: ~2.5x performance improvements with filtering

## Slide 60: Filtering – Accurate but Costly Sorting
Software-based filtering heuristics aim to reduce unnecessary computations
  High-accuracy can be achieved with filtering with correct setting
Filtering takes up ~8.5% of the overall execution time due to sorting

## Slide 61: Choosing the Right Amount of Cores
We analyze maximum number of cores that ApHMM can utilize
  Before it is bottlenecked by memory bandwidth for genomics applications
ApHMM with 4 cores (ApHMM-4) provides the best overall speedup

## Slide 62
HiPEAC 2024
Accelerating Profile Hidden Markov Models for Fast and Energy-Efficient Genome Analysis
ApHMM
Paper
Kamlesh Pillai, Gurpreet S. Kalsi, Bharathwaj Suresh, Damla Senol Cali, Jeremie S. Kim, Taha Shahroodi, Meryem Banu Cavlak, Joël Lindegger, Mohammed Alser, Juan Gómez Luna, Sreenivas Subramoney, Onur Mutlu
Can Firtina
canfirtina@gmail.com
https://cfirtina.com