## Slide 1
via Algorithm-Architecture Co-Design
Accelerating AI-Driven Genome Analysis
Can Firtina | canfirtina@gmail.com
Senior Researcher and Lecturer at ETH Zurich
Incoming Assistant Professor of Computer Science at UMD
June 16, 2025
PASC25, Challenges in Systems Design for Omics, Switzerland

## Slide 2: The Goal of Computing: Beyond Numbers
“The purpose of computing is [to gain] insight, not numbers”
Richard Hamming
"Numerical Methods for Scientists and Engineers," Richard Hamming, 1962.

## Slide 3: Big Data is Everywhere
Large recommender systems
Large Language Models
Graph/Tree Processing
Genomics

## Slide 4: Computing is Bottlenecked by Data
Large recommender systems
Large Language Models
Graph/Tree Processing
Genomics
Data movement → Performance & Energy Bottleneck

## Slide 5: Problems with Data Analysis Today
Special-Purpose Machine
for Data Generation
FAST
General-Purpose Machine
for Data Analysis
SLOW
Processing capabilities oblivious to data analysis requirements
Large amounts of data movement

## Slide 6: Data Movement Dominates Performance
Microprocessor
Main Memory
Storage (SSD/HDD)
Sequencing
Machine
Data movement dominates performance and is a major system energy bottleneck (accounting for 40% - 62%)
- Boroumand et al., “Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks,” ASPLOS 2018
- Kestor et al., “Quantifying the Energy Cost of Data Movement in Scientific Applications,” IISWC 2013
- Pandiyan and Wu, “Quantifying the energy cost of data movement for emerging smart phone workloads on mobile platforms,” IISWC 2014
Data Movement
Single memory request consumes >160 - 800 more energy compared to performing an addition operation

## Slide 7: We need to co-design algorithms and architecture to handle data well

## Slide 8: Pushing Towards New Architectures
GPUs
Heterogeneous
Processors &
Accelerators
Hybrid Main Memory
Persistent Memory/Storage
FPGAs
Modern systems
?
Sequencing Machine

## Slide 9: Pushing Towards New Architectures
GPUs
Heterogeneous
Processors &
Accelerators
Hybrid Main Memory
Persistent Memory/Storage
FPGAs
Modern systems
?
Sequencing Machine

## Slide 10: Algorithm-Architecture Co-design is Critical
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Computer Architecture (expanded view)

## Slide 11: Accelerating Genome Analysis [DAC '23]
Onur Mutlu and Can Firtina, "Accelerating Genome Analysis via Algorithm-Architecture Co-Design" Invited Special Session Paper in Proceedings of the 60th Design Automation Conference (DAC), San Francisco, CA, USA, July 2023. [Related Invited Paper] [arXiv version] [Slides (pptx) (pdf)] [Talk Video at DAC 2023] (38 minutes, including Q&A)

## Slide 12: Analyzing Genomes Reveals Key Insights
Detecting pathogens in the environment
Rapid surveillance of disease outbreaks
Altering genomes to solve fundamental challenges of life
Personalized Medicine

## Slide 13: Generating the Entire Genomic Sequence
Whole Genome: 6.4B bps
(Non-human-readable)
CGAAATGCC...AGATTAAACGCT...TGCCCTAA...GAATGGCGT
Whole Human Genome: 6.4B bps (Human-readable)
Raw Genomic Data (Human-readable?)
Sequencing Device
Translator (Basecalling)
AI

## Slide 14: Genomic Data: Giant Jigsaw Puzzle to Solve
CGAAATGCC...AGATTAAACGCT...TGCCCTAA...GAATGGCGT
Human (Reference) Genome: 3.2 Billion bps (haploid)
Unknown origins
?
Non-identical reference genome
Small pieces (reads)
Large volume of data to analyze
AAATGG
Read: ~100 – 100,000 bps
?
Scale: ~
CGAAATGCC...AGATTAAATGGT...TGCCCTAA...GAATGGCGT
Entire Genomic Sequence of an Organism
Data Science for Massive Datasets (TBs to PBs)

## Slide 15: A Common Genome Analysis Pipeline
Assembly
Variant Calling
Metagenomics
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
Downstream Analysis
Raw Reads
Read Mapping
Basecalling (Translator)
AAATGTGGTCCATTG
Basecalled (Translated) Reads

## Slide 16: Genome Analysis is Energy Inefficient
Raw Reads
Read Mapping
Basecalling (Translator)
AAATGTGGTCCATTG
Basecalled (Translated) Reads
- Boroumand et al., “Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks,” ASPLOS 2018
- Kestor et al., “Quantifying the Energy Cost of Data Movement in Scientific Applications,” IISWC 2013
- Pandiyan and Wu, “Quantifying the energy cost of data movement for emerging smart phone workloads on mobile platforms,” IISWC 2014
Single memory request consumes >160 - 800 more energy compared to performing an addition operation
Costly and large volumes of data movement
Power-Hungry Devices

## Slide 17: Genome Analysis is Computationally Costly
Chart: Runtime (Hour)
| Basecalling + Read Mapping | Assembly
Heterogeneous System (with CPUs and GPUs) | 16 | 1.5
Significant computation and energy overhead

## Slide 18: Limited Application Scope and Accuracy
Energy-efficient analysis for Resource-constrained devices
Urgent analysis within minutes
Large-scale analysis without sacrificing accuracy and performance

## Slide 19: Enabling New Directions in Genome Analysis via New Algorithms

## Slide 20: New Frontiers: Raw Signal Analysis [ISMB '23]
Can Firtina, Nika Mansouri Ghiasi, Joel Lindegger, Gagandeep Singh, Meryem Banu Cavlak, Haiyu Mao, and Onur Mutlu, "RawHash: Enabling Fast and Accurate Real-Time Analysis of Raw Nanopore Signals for Large Genomes" Proceedings of the 31st Annual Conference on Intelligent Systems for Molecular Biology (ISMB) and the 22nd European Conference on Computational Biology (ECCB), July 2023 [Online link at Bioinformatics Journal] [arXiv version] [Slides (pptx) (pdf)] [Talk Video at ISMB/ECCB 2023] (19 minutes) [RawHash Source Code]

## Slide 21: Real-Time Raw Signal Analysis [Bioinformatics '24]
Can Firtina, Melina Soysal, Joël Lindegger, and Onur Mutlu, "RawHash2: Mapping Raw Nanopore Signals Using Hash-Based Seeding and Adaptive Quantization" Bioinformatics, July 2024. [Online link at Bioinformatics Journal] [arXiv version] [RawHash Talk Video] (19 minutes) [RawHash2 Source Code]

## Slide 22: New Directions: Assembling Raw Signals
Can Firtina, Maximilian Mordig, Harun Mustafa, Sayan Goswami, Nika Mansouri Ghiasi, Stefano Mercogliano, Furkan Eris, Joël Lindegger, Andre Kahles, and Onur Mutlu "Rawsamble: Overlapping and Assembling Raw Nanopore Signals using a Hash-based Seeding Mechanism" arXiv, October 2024 [arXiv version] [Talk Video at CSHL Data Science 2024] (16 minutes) [Source Code]
arXiv
Source code

## Slide 23: Quickly Aligning Raw Signals [IEEE Access '24]
Joel Lindegger, Can Firtina, Nika Mansouri Ghiasi, Mohammad Sadrosadati, Mohammed Alser, and Onur Mutlu, "RawAlign: Accurate, Fast, and Scalable Raw Nanopore Signal Mapping via Combining Seeding and Alignment" IEEE Access, December 2024. [Online link at IEEE Access Journal] [arXiv version] [RawAlign Source Code]

## Slide 24: In-Storage Raw Signal Analysis [ICS '25]
Melina Soysal, Konstantina Koliogeorgi, Can Firtina, Nika Mansouri Ghiasi, Rakesh Nadig, Haiyu Mao, Geraldo Francisco Oliveira Junior, Yu Liang, Klea Zambaku, Mohammad Sadrosadati, and Onur Mutlu "MARS: Processing-In-Memory Acceleration of Raw Signal Genome Analysis Inside the Storage Subsystem" In 39th International Conference on Supercomputing (ICS), June 2025. [arXiv version]

## Slide 25: Tolerating Noise in String Matching [NARGAB '23]
Can Firtina, Jisung Park, Mohammed Alser, Jeremie S. Kim, Damla Senol Cali, Taha Shahroodi, Nika Mansouri Ghiasi, Gagandeep Singh, Konstantinos Kanellopoulos, Can Alkan, Onur Mutlu, "BLEND: A Fast, Memory-Efficient, and Accurate Mechanism to Find Fuzzy Seed Matches in Genome Analysis" NAR Genomics and Bioinformatics, March 2023. [Online link at NAR Genomics and Bioinformatics Journal] [arXiv version] [bioRxiv version] [Talk Video at RECOMB 2023] (23 minutes) [BLEND Source Code]

## Slide 26: Mitigating Useless Computations [IEEE/ACM TCBB '24]
Jeremie S. Kim*, Can Firtina*, Meryem Banu Cavlak, Damla Senol Cali, Nastaran Hajinazar, Mohammed Alser, Can Alkan, and Onur Mutlu, "AirLift: A Fast and Comprehensive Technique for Remapping Alignments between Reference Genomes" IEEE/ACM TCBB, August 2024. [Online link at IEEE/ACM TCBB Journal] [arXiv version] Presented at the 21st Asia Pacific Bioinformatics Conference (APBC), Changsha, China, April 2023. [Slides (pptx) (pdf)] [Talk Video at BIO-Arch 2023 Workshop] (22 minutes) [AirLift Source Code]
*Equal contribution

## Slide 27: Mitigating Useless Computations [Bioinformatics '22]
Jeremie S. Kim, Can Firtina, Meryem Banu Cavlak, Damla Senol Cali, Can Alkan, and Onur Mutlu, "FastRemap: A Tool for Quickly Remapping Reads between Genome Assemblies" Bioinformatics, October 2022. [Online link at Bioinformatics Journal] [arXiv preprint] [FastRemap Source Code]

## Slide 28: Utilizing AI/ML in Genome Analysis via New Algorithms and Architectures

## Slide 29: Error Correction using ML [Bioinformatics '20]
Can Firtina, Jeremie S. Kim, Mohammed Alser, Damla Senol Cali, A. Ercument Cicek, Can Alkan, and Onur Mutlu, "Apollo: A Sequencing-Technology-Independent, Scalable, and Accurate Assembly Polishing Algorithm" Bioinformatics, June 2020. [Online link at Bioinformatics Journal] [arXiv version] [Slides (pptx)][(pdf)] [Source Code]

## Slide 30: Accelerating ML & Genome Graphs [ACM TACO '24]
Can Firtina, Kamlesh Pillai, Gurpreet S. Kalsi, Bharathwaj Suresh, Damla Senol Cali, Jeremie S. Kim, Taha Shahroodi, Meryem Banu Cavlak, Joel Lindegger, Mohammed Alser, Juan Gomez Luna, Sreenivas Subramoney and Onur Mutlu, "ApHMM: Accelerating Profile Hidden Markov Models for Fast and Energy-efficient Genome Analysis" ACM Transactions on Architecture and Code Optimization (TACO), Feb 2024. [ACM Digital Library version] [arXiv version] Presented at the 19th HiPEAC Conference, Munich, Germany, January 2024. [Slides (pptx) (pdf)] [Talk Video HiPEAC 2024] (35 minutes) [ApHMM Source Code]

## Slide 31: Translating Raw Signals using ML [Genome Biology '24]
Gagandeep Singh, Mohammed Alser, Kristof Denolf, Can Firtina, Alireza Khodamoradi, Meryem Banu Cavlak, Henk Corporaal and Onur Mutlu, "RUBICON: A Framework for Designing Efficient Deep Learning-Based Genomic Basecallers" Genome Biology, February 2024. [arXiv version] [Online link at Genome Biology Journal] [RUBICON Source Code]

## Slide 32: Eliminating Useless Basecalling [Frontiers In Genetics '24]
M. Banu Cavlak, Gagandeep Singh, Mohammed Alser, Can Firtina, Joel Lindegger, Mohammad Sadrosadati, Nika Mansouri Ghiasi, Can Alkan, and Onur Mutlu, "TargetCall: Eliminating the Wasted Computation in Basecalling via Pre-Basecalling Filtering" Frontiers in Genetics, October 2024. [Online link at Frontiers in Genetics Journal] [arXiv Version] [Talk Video at BIO-Arch 2023 Workshop] [TargetCall Source Code]

## Slide 33: Basecalling using PIM [MICRO '23]
Taha Shahroodi, Gagandeep Singh, Mahdi Zahedi, Haiyu Mao, Joel Lindegger, Can Firtina, Stephan Wong, Onur Mutlu, and Said Hamdioui, "Swordfish: A Framework for Evaluating Deep Neural Network-based Basecalling using Computation-In-Memory with Non-Ideal Memristors" Proceedings of the 56th International Symposium on Microarchitecture (MICRO), Toronto, ON, Canada, November 2023. [Slides (pptx) (pdf)] [arXiv version]

## Slide 34: DNN Hardware Acceleration
DNN execution is dominated by:
Memristor-based crossbars support VMM
Vector-Matrix Multiplication (VMM)
Data movement between memory and accelerator
(e.g., GPU or TPU)
Processing in Memory (PIM) minimizes data movement
Memristor-based PIM for DNN Acceleration
  [Ankit+, ASPLOS 2019], [Chi+, ISCA 2016], [Lou+, PACT2020], [Shafiee+, ISCA 2016]

## Slide 35: VMM in Memristor-based Crossbars
Digital to Analog Converters
Analog to Digital Converters

## Slide 36: Non-idealities in Memristor-based Crossbars
Digital to Analog Converters
Analog to Digital Converters
Non-ideal DAC
Variation in
Synaptic Conductance
Wire Resistance
Non-ideal ADC
Subpar utilization of trained models due to non-idealities

## Slide 37: Accuracy: All Non-idealities without Mitigation
Non-idealities
Accuracy (%)
D1
D2
Baseline
Baseline
Combined non-idealities leads to significant accuracy loss (>18%)

## Slide 38: Accuracy: Enhancement Techniques on All Non-idealities
D1
Accuracy (%)
Baseline
Baseline
D3
Accuracy loss drops to 6% from 18% after handling all non-idealities
Enhancement Technique

## Slide 39: ML-based Genome Analysis via PIM [MICRO '22]
Haiyu Mao, Mohammed Alser, Mohammad Sadrosadati, Can Firtina, Akanksha Baranwal, Damla Senol Cali, Aditya Manglik, Nour Almadhoun Alserr, and Onur Mutlu, "GenPIP: In-Memory Acceleration of Genome Analysis via Tight Integration of Basecalling and Read Mapping" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (25 minutes)] [arXiv version]

## Slide 40: Problem 1: Large Data Movement
Raw Signals
Basecalling
Reads
Read quality
control
High-quality
reads
Read
mapping
Mapped
reads
Large data movement between genome analysis steps
3913 GB
546 GB
437 GB
382 GB
[NC'19] Rory Bowden, Robert W Davies, Andreas Heger, Alistair T Pagnamenta, Mariateresa de Cesare, Laura E Oikkonen, Duncan Parkes, Colin Freeman, Fatima Dhalla, Smita Y Patel, et al. Sequencing of human genomes with nanopore technology. Nature Communications, 2019.

## Slide 41: Problem 2: Wasted Computation
Raw Signals
Basecalling
Reads
Read quality
control
High-quality
reads
Read
mapping
Mapped
reads
Low-quality
reads
Unmapped
reads
A considerable amount of computation on useless data due to
Low-quality reads
Unmapped reads
100%
79.5%
69.5%
20.5%
10%

## Slide 42: Goal and Opportunities
Chart: Normalized Speedup
| System A | System B | System C
Normalized Speedup | 2.7 | 6.1 | 9
We perform a study to quantify potential performance benefits
Goal: Efficiently accelerate the entire genome analysis pipeline while minimizing data movement and useless computation
NVM-based PIM accelerators for separate basecalling and read mapping
no data movement
between the accelerators of analysis steps
no data movement
and
no useless reads
(ideal case)

## Slide 43: GenPIP Overview
GenPIP
Read Mapping Module
GenPIP Controller
Basecalling Module
eDRAM
In-memory
Read Mapping
[PARC, ASPDAC’20]
+ Our design
In-memory
Basecaller
[Helix, PACT’20]
PIM-CQS
PIM chunk quality score calculation
Raw signals from the sequencing machine
Signal
chunk
Base quality score
Chunk mapping score
To storage
Read mapping result
Average Calculator
ER
ER
Controller
Quality score
ER
Chunk
Read Mapping Controller
Basecalled
chunk
Chunk quality score
https://arxiv.org/pdf/2209.08600.pdf

## Slide 44
Fast, Accurate, and Efficient Genome Analysis via Algorithm-Architecture co-design

## Slide 45: Accelerating String Matching [MICRO '20]
Damla Senol Cali, Gurpreet S. Kalsi, Zulal Bingol, Can Firtina, Lavanya Subramanian, Jeremie S. Kim, Rachata Ausavarungnirun, Mohammed Alser, Juan Gomez-Luna, Amirali Boroumand, Anant Nori, Allison Scibisz, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis" Proceedings of the 53rd International Symposium on Microarchitecture (MICRO), Virtual, October 2020. [Lightning Talk Video (1.5 minutes)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (18 minutes)] [Slides (pptx) (pdf)]

## Slide 46: Accelerating Genome Graphs [ISCA '22]
Damla Senol Cali, Konstantinos Kanellopoulos, Joel Lindegger, Zulal Bingol, Gurpreet S. Kalsi, Ziyi Zuo, Can Firtina, Meryem Banu Cavlak, Jeremie Kim, Nika Mansouri Ghiasi, Gagandeep Singh, Juan Gomez-Luna, Nour Almadhoun Alserr, Mohammed Alser, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "SeGraM: A Universal Hardware Accelerator for Genomic Sequence-to-Graph and Sequence-to-Sequence Mapping" Proceedings of the 49th International Symposium on Computer Architecture (ISCA), New York, June 2022. [Slides (pptx) (pdf)] [arXiv version] [SeGraM Source Code and Datasets] [Talk Video (22 minutes)]

## Slide 47: In-Storage Filtering for Genomics [ASPLOS '22]
Nika Mansouri Ghiasi, Jisung Park, Harun Mustafa, Jeremie Kim, Ataberk Olgun, Arvid Gollwitzer, Damla Senol Cali, Can Firtina, Haiyu Mao, Nour Almadhoun Alserr, Rachata Ausavarungnirun, Nandita Vijaykumar, Mohammed Alser, and Onur Mutlu, "GenStore: A High-Performance and Energy-Efficient In-Storage Computing System for Genome Sequence Analysis" Proceedings of the 27th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, Feb 2022. [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (90 seconds)]

## Slide 48: In-Storage Metagenomics [ISCA '24]
Nika Mansouri Ghiasi, Mohammad Sadrosadati, Harun Mustafa, Arvid Gollwitzer, Can Firtina, Julien Eudine, Haiyu Mao, Joel Lindegger, Meryem Banu Cavlak, Mohammed Alser, Jisung Park, and Onur Mutlu, "MegIS: High-Performance and Low-Cost Metagenomic Analysis with In-Storage Processing" Proceedings of the 51st Annual International Symposium on Computer Architecture (ISCA), Buenos Aires, Argentina, July 2024. [Slides (pptx) (pdf)] [arXiv version]

## Slide 49: Accelerating Genome Analysis [DAC '23]
Onur Mutlu and Can Firtina, "Accelerating Genome Analysis via Algorithm-Architecture Co-Design" Invited Special Session Paper in Proceedings of the 60th Design Automation Conference (DAC), San Francisco, CA, USA, July 2023. [Related Invited Paper] [arXiv version] [Slides (pptx) (pdf)] [Talk Video at DAC 2023] (38 minutes, including Q&A)

## Slide 50: Overview of Our Research Interests
Today’s Talk
Algorithm & Hardware Design for AI in Genome Analysis
[Bioinformatics'20]
[ACM TACO'24]
[Genome Biology'24]
[Front. in Genetics'24]
Real-Time and Raw Sequencing Data Analysis
[ISMB/ECCB'23]
[Bioinformatics'24]
[IEEE Access'24]
[arXiv'24 & HiTSeq'24]
Accurate and Fast Algorithm Design for Read Mapping
[Bioinformatics'22]
[NARGAB'23 & RECOMB'23]
[arXiv'23]
[arXiv'23]
[IEEE/ACM TCBB'24]
Data-Centric Architectures for Genome Analysis
[MICRO'20]
[MICRO'22]
[ISCA'22]
[ASPLOS'22]
[IEEE Access'22]
[MICRO'23]
[ISCA'24]
Reviews [CSBJ'22] [DAC'23] [Nature Protocols'24]
Goal: Enable Fast, Energy-Efficient, Accurate, and Scalable Genome Analysis by Designing Algorithms and Architectures

## Slide 51: Today’s Talk
Significant computation and energy overhead
Limited accuracy and application scope
Algorithm & Hardware Design for AI in Genome Analysis
ApHMM (TACO'24 & HiPEAC'24)
  Accelerating ML operations in Genome Graphs

## Slide 52: General-Purpose "Things"

## Slide 53: Algorithm Design Demands General-Purpose Computing
Function 2
Function 4
General-Purpose Systems
(e.g., CPUs)
Function 1
Function 3
Your Favorite Output
Your Favorite Algorithm
Paid Costs for Generality:
Supporting unnecessary operations
Inefficient data and control flow
Limited parallelism & bandwidth
High latency &
Substantial energy

## Slide 54: Great Algorithms Demand Specialization
Goal: Avoid wasting computation & energy
Opportunities: Better data flow with minimal latency & power
Everyone’s Favorite Algorithm
Function 2
Function 1
Function 3
Function 1
Function 2
Function 3
Application-Specific Architecture
Paid Costs for Specialization:
Poor programmability
High manufacturing and engineering costs
Efficient processors customized for the task
Better parallelism

## Slide 55: Acceleration Efforts for AI and Genomics
Google’s TPUs:
Cerebras WSE-3 The largest ML accelerator chip
NVIDIA H100

## Slide 56
Important and Commonly Used Applications Demand Specialization

## Slide 57: Probabilistic Graphs in Genomics
Probabilistic graphs are commonly used to identify variations between sequences
To avoid redundant comparisons and storage
To provide rich information
on expected variations
Reference Genome Graph

## Slide 58: Graph-Based Applications in Genomics
Protein
Protein
Family #1
Protein
Family #2
Protein Family Search
with Graph Alignment
GCCCATATGGTTAAGCTT
CCCT
TGCT
GCTA
CCTA
GCTT
ATGC
AAGC
CCCT
GCTT
GCCCTTATGCTTAAGCTA
Error Correction with Probabilistic Graphs
GCCC-TATGGTTAAGCTT
GCCCATATGATTAAGCTT
GCCCATATGGTTAAGCTT
GCCCATATGGTTAAGCTT
GCCCGTATGGTT--GCTT
GCCCATATGCTTAAGCTT
GCCC---TGGTTAAGCT-
GCCCATATCCTTAAGCTT
Multiple Sequence Alignment

## Slide 59: A Common Graph Structure in Genomics
A
C
T
T
D
I
I
I
I
D
D
A: 0.1
T: 0.2
G: 0.6
C: 0.1
A: 0.9
T: 0.1
G: 0.0
C: 0.0
A: 0.1
T: 0.1
G: 0.1
C: 0.7
A: 0.2
T: 0.2
G: 0.2
C: 0.4
0.2
0.4
0.7
0.6
0.3
0.1
Profile Hidden Markov Models (PHMMs): A probabilistic graph structure

## Slide 60: Underlying ML Technique in Genomic Graphs
Forward Calculations
Backward Calculations
Updating Transition Probabilities
Updating Emission Probabilities

## Slide 61: Underlying ML Technique in Genomic Graphs
Forward Calculations
Backward Calculations
Function 1
Function 1
Function 2
Function 2
Function 3
Function 4
Updating Transition Probabilities
Updating Emission Probabilities

## Slide 62: Costly Use of ML in Genomic Graphs
45.76%
51.44%
98.57%
Cost of Using Machine Learning (ML) in pHMMs:

## Slide 63: Goal
Enable rapid and power-efficient use of the underlying ML technique in genome graphs

## Slide 64: Key Approach: HW-SW Co-Design
SW
HW
Reduce redundant data storage by utilizing the fixed data pattern
Reduce unnecessary computations with quick filtering
Avoid repeated operations by utilizing lookup tables
Reduce data movement by processing data where it makes sense
Flexible and efficient hardware design

## Slide 65: HW: Simple Data Pattern in DP Calculations
A
T
G
T
Simple Pattern
A
D
I
D
C
I
D
T
I
Store and access data where it makes sense
Many Different Patterns
Dynamic Programming (DP) Operations:
DP Operations in pHMMs:
Frequent off-chip access
DP Computation in pHMMs
Fast On-chip Memory Access
MUL
ADD
FP DIV
MUL

## Slide 66: SW: Reducing Unnecessary Computations
A
T
G
T
Dense DP Calculations
A
D
I
D
C
I
D
T
I
Sparse (Filtered) DP Calculations
A
D
I
D
C
I
D
T
I
A
T
G
T
Filter by sorting
Observation: Calculating the entire DP is not needed
Challenge: Sorting is costly in hardware

## Slide 67: SW: Reducing Unnecessary Computations
Histogram Filter
.
.
.
8, 9
10, 14
15, 16, 18
11, 20, 21, …
13, 17, 19, …
State IDs
Range
1.00 – 0.94
0.94 – 0.88
0.88 – 0.82
0.82 – 0.76
0.76 – 0.70
0.06 – 0.00
.
.
.
Software co-design: Replace sorting with a cheaper filtering

## Slide 68: Putting the Optimizations Together
Effectively implementing the hardware and software optimizations to improve performance and reduce power requirements

## Slide 69: Integrating ApHMM in a Complete System
The specialized task can be offloaded to an accelerator whenever needed

## Slide 70: Key Results: Performance
Specialized design enables computation up to two orders of magnitude faster:
Better data flow with reduced latency and improved parallelism
Chart: Speedup Over CPU (1 Thread)
| Algorithm Acceleration
CPU (32 Threads) | 23.0925
GPU | 74.9956
ApHMM | 260.0273

## Slide 71: Key Results: Energy Consumption
…and a significant reduction in energy consumption by up to three orders of magnitude: simpler hardware with a minimized off-chip memory accesses and data movement
Chart: Energy Reduction Over CPU
| Algorithm Acceleration
CPU | 1
GPU | 1.4528
ApHMM | 2474.0912

## Slide 72
Specialization Provides Significant Performance and Energy Benefits

## Slide 73: Today’s Talk
Significant computation and energy overhead
Limited accuracy and application scope
Algorithm & Hardware Design for AI in Genome Analysis
ApHMM (TACO'24 & HiPEAC'24)
  Accelerating ML operations in Genome Graphs

## Slide 74: Summary of Key Takeaways
There are many ways to utilize AI in genomics (and life sciences more broadly)
  We only scratched the surface of those applications today
It is critical to consider the requirements of your application
  Portable? Low latency? Highest accuracy?
It is critical to consider the limitations of your system
  And integrate these limitations in the analysis
Data movement will continue to be a major system bottleneck
  Generating biological data is getting faster and cheaper
Many future opportunities exists with emerging technologies

## Slide 75: Acknowledgements
Collaborators:
Funding agencies and industry sponsors:
  BioPIM, SNSF, Intel, Google, Huawei, Microsoft, VMware, and SRC

## Slide 76
via Algorithm-Architecture Co-Design
Accelerating AI-Driven Genome Analysis
Can Firtina | canfirtina@gmail.com
Senior Researcher and Lecturer at ETH Zurich
Incoming Assistant Professor of Computer Science at UMD
June 16, 2025
PASC25, Challenges in Systems Design for Omics, Switzerland